## Slide 1: Layer 2 Interconnecting Devices
Team 2:
Adelmo Amarö
David Congreve
Chris McKeague
Joel Schrader

## Slide 2: Purpose
Hardware device, operates in Layer 2
Connects two attached network nodes
Receives data and transforms into frames or vice versa

## Slide 3: Type of devices
Bridges
Multiplexers
Layer 2 Switches

## Slide 4: Multiplexers
Combines 2 or more I/P in a single medium
A “multiplexer” contains both MUX and DEMUX
Cheaper, less channels, less network circuits

## Slide 5: Multiplexing
There a number of different multiplexing methodologies
Multiplexing Method | Technological Application
Code Division Multiplexing (CDMA) | 2G Mobile phones 3G Mobile phone networks (uses WCDMA) IEEE802.11 (wifi)
Frequency Division Multiplexing (FDM) | Wifi IEEE802.11 a/b/g/n Digital radio and television IEEE802.16 Analogue telephone networks ZigBee

## Slide 6: Multiplexing
Multiplexing Method | Technological Application
Time Division Multiplexing (TDM) | GSM mobile phone networks Digital telephone networks Bluetooth DSLAMs (also known as CMUX)
Wavelength Division Multiplexing (WDM | Wired digital networks

## Slide 7: Code Division Multiple Access (CDMA)
CDMA uses spread spectrum technology that was initially developed by the military during WWII. Main development performed by QUALCOM.
Current generation CDMA phones utilise DSSS (Direct Sequence Spread Spectrum)

## Slide 8: Code Division Multiple Access (CDMA)
Allows multiple signals to be transmitted over a single medium by the use of a unique code for each device that connects to the network
On transmission this code is applied to the data signal
All signals are transmitted at the same frequency and then have a situation where constructive interference occurs

## Slide 9: Code Division Multiple Access (CDMA)
Key Features
Each user has unique PN (pseudo noise) code
System performance degrades for all users as number of concurrent users increases (soft capacity limit)
Interference mitigated
Near-Far Problem – modules further from the base station transmit at higher power to those close to ensure that power of all signals is similar (enables filtering of noise more easily)

## Slide 10: Code Division Multiple Access (CDMA)
Transmitted data = DATA xor CODE
Transmitted data = DATA xor CODE
Constructive interference of transmitted signals
De-multiplexing
Composite signal dot product with CODE
Change in sign denotes binary 1 or 0 in original signal

## Slide 11: Code Division Multiple Access (CDMA)
New methods of utilising this concept are being developed and are forming the basis for the next generation of mobile networks (3G)
TD-SCDMA: Time Division – Synchronous Code Division Multiple Access
W-CDMA: Wideband Code Division Multiple Access

## Slide 12: Frequency Division Multiplexing
How it works?
Frequency Division Multiplexing (FDM) is a scheme in which numerous signals all assigned a different frequencies are combined for transmission on a single communication line.
Each signal travels within its own unique frequency range (carrier), which is modulated by the data (text, voice, video, etc.).

## Slide 13: Frequency Division Multiplexing
20kHz spectrum divided in 4kHz channels for the 5 sources.

## Slide 14: Frequency Division Multiplexing
What is it used for?
The most common uses for FDM are listed below:
- Old analog POTS
- ADSL IEEE802.2
- WiFi IEEE802.11a/b/g/n
- Digital Radio and Video IEEE802.16

## Slide 15: Frequency Division Multiplexing

## Slide 16: Time Division Multiplexing
How it works?
  Multiple signals carried out on a single channel by interleaving pulses in time domain
  Interleaving pulses – Time Frames - takes turns on a single channel
  Each signal can occupy entire BW
  Encoding using PCM, PCM -TDM
  More efficient than FDM

## Slide 17: Time Division Multiplexing

## Slide 18: Time Division Multiplexing

## Slide 19: Time Division Multiplexing
Types:
  Synchronous Time Division Multiplexing
  Statistical Time Division Multiplexing

## Slide 20: Time Division Multiplexing
Synchronous TDM
  Each time frame allocated to a channel is fixed
  Time frame allocated even if not data available
  Time frames rotates including empty frames
  Wastes BW
  Used in ISDN and T1 phone lines

## Slide 21: Time Division Multiplexing

## Slide 22: Time Division Multiplexing
Statistical TDM
  Also known as Asynchronous TDM
  Uses variable length time frames, used as demanded
  If station is active, Statistical MUX collects data and creates a frame with this data only
  Avoids time slots to be wasted
  More complex than Synch TDM, more expensive

## Slide 23: Time Division Multiplexing

## Slide 24: Wavelength Division Multiplexing
Technology which multiplexes multiple optical carrier signals on a single optical fibre by using different wavelengths of laser light to carry different signals
Enables the utilization of a significant portion of the available fiber bandwidth by allowing many independent signals to be transmitted simultaneously on one fiber

## Slide 25: Wavelength Division Multiplexing
Wavelength Division Multiplexing

## Slide 26
Wavelength Division Multiplexing
Wavelength Division Multiplexing

## Slide 27
Wavelength Division Multiplexing Types
WDM systems are divided into two groups; dense and coarse Wavelength Division multiplexing.
Dense Wavelength Divison Multiplexing (DWDM) are systems with more than 8 active wavelengths per fibre
Coarse Wavelength Division Multiplexing are systems with fewer than eight active wavelengths per fibre
Wavelength Division Multiplexing

## Slide 28: Wavelength Division Multiplexing
WDM Major System Components
An optical laser (transmitter).
An optical detector (receiver).
Optical filters for multiplexing (add) and demultiplexing (drop).
Optical amplifiers for distance extension.

## Slide 29: Wavelength Division Multiplexing
Wavelength Division Multiplexing
Basic application of WDM is for the transmission of e-mail, video, multimedia, data, and voice carried over an optical network.

## Slide 30: Network Switch
A network switch is a device that connects network segments
Switches can connect Ethernet, Token Ring, Fibre Channel or other types of packet switched network segments

## Slide 31: Network Switch
Basic Operation
A frame enters a switch, the switch saves the originating MAC address, and the originating port in the switch's MAC address table. The switch then selectively transmits the frame from specific ports based on the frame's destination MAC address

## Slide 32: Network Switch
Forwarding Methods
Store and Forward
Cut through
Fragment free
Adaptive Switching

## Slide 33: Network Switch
Switching mode: | Defects: | Then, adaptive mode changes the switching mode to:
Cut-through | High numbers of CRC errors | Store-and-forward
 | High numbers of runts | Fragment-free
Fragment-free | High numbers of CRC errors | Store-and-forward
 | Low numbers of runts | Cut-through
Store-and-forward | Low numbers of CRC errors | Fragment-free
 | Low numbers of CRC errors and runts | Cut-through
Adaptive Switching

## Slide 34: Network Switch
Switched Network, Full duplex ability

## Slide 35: Bridges
Operation
  Read all frames transmitted from one LAN and accept address from the other LAN
  Data is read at the physical address level MAC
  Independent of protocols, Bridge looks only for MAC address
  In a complex situation bridges make routing decision

## Slide 36: Bridges

## Slide 37: Bridges

## Slide 38: Bridges
Purpose
  Connect as a node in a network providing interconnection with other LAN
  Can learn network topology and address of all devices in the LAN by building a bridging table with all network addresses
  Reduces LAN traffic congestion by eliminating frames not need it to be forwarded
  Protects LAN against intruders by blocking the MAC address

## Slide 39: Bridges
Types of Bridging
  Transparent
    Used in Ethernet Networks
    Build an address table as they receive data
    Each bridge has two ports and the address table is associated with it
    If address is not in bridge table, data is forwarded to all segments other than the one it came from

## Slide 40: Bridges

## Slide 41: Bridges
Types of Bridging
  Source
    Used in Token Ring Networks
    Source routing bridges do not learn from watching tables
    Station needs to know the exact path of the network to send the frame
    If station doesn’t know the exact path, it send a “discovery” frame and when it returns, it records the path
    Sending station sends the path to be transmitted

## Slide 42: Bridges

## Slide 43: Switch vs. Bridge
Bridge frame handling done in software
Switch performs address recognition and frame forwarding in hardware
Bridge only analyzes and forwards one frame at a time
Switch can handle multiple frames at a time
Bridge uses store-and-forward operation
Switch can have cut-through operation

## Slide 44: Questions