## Slide 1: Wireless LAN
CSMA A-Division:
Adelmo Amarö
David Congreve
Chris McKeague
Joel Schrader

## Slide 2: Overview
Transfer data using RF an IR signals
Complement to a wired LAN, not a substitute for wired LAN
Access points link wired LAN with wireless LAN

## Slide 3: Applications
Eases relocation and other modification to network structure
Provides a link between a LAN server and a mobile client such as laptop or PDAs
Extends the wired LAN services to open areas unable to install a wired connection.
In some cases it can replace wired LANs if wired LANs are not an option (e.g. asbestos buildings)
Notes: PDA Personal digital assistant
Extends the wired LAN services to open areas unable to install a wired connection such as campus or open areas for example the university campus to be accessible at any point to connect to the LAN without going to the connection
Or if the cost of the wired LAN installation is too expensive and not feasible

## Slide 4: Types of Wireless LAN
Wireless Standard | Common Sub-standards | Typical Applications
IEEE 802.11x (WLAN) | IEEE 802.11a,b,g | Wifi networks with high speed data access over a wide area for notebook and PDA computers
IEEE 802.15.x (WPAN) | IEEE 802.15.1 – Bluetooth IEEE802.15.3 – Wireless USB IEEE 802.15.4 – Zigbee | Short range wireless connectivity for peripheral devices

## Slide 5: RF Propagation
Transmit signals at 902-928MHz, 2.4-2.4835GHz, or 5-5.5825GHz
Line-of-sight transmission
Uses Omni directional antennae
Used for short distance communications
Operates in the Industrial, Scientific and Medical (ISM) band which does not require licences
Uses Spread Spectrum Transmission
Suffers from interference and propagation problems:
  Attenuation
  Shadow spots
  Multipath interference and Rayleigh fading
  EM interference
Notes: Bands above 30MHz are line of sight waves.
LANs operates in an unlicensed radio bands known as Industrial, Scientific and Medical (ISM ) band which does not require licences; the requirement of licences will make WLAN an uneconomical option
Regulators required that WLAN must use Spread Spectrum Transmission
Rayleigh fading occurs when the difference in path length of the same signal arriving along different paths is a multiple of half the wavelenght, this causes the signal to be almost completely cancel out at the receiver

## Slide 6
Attenuation: signal gets
weaker with distance
Shadow
Zone
(Dead Spot)
Electromagnetic
Interference
(EMI) from
Other stations,
Microwave ovens, etc.
Reflected Signal
Laptop
Direct Signal
Multipath
Interference
Direct and reflected signals may cancel out (Rayleigh fading)
Blocking
Object
Notes: Signals may bounce off floors or buildings, interfering with direct signals and even cancel out signals opposite in phase. In television, this happens in large cities, where TV signals bounce off buildings producing “ghosting” in which faint images appear slightly displaced from the original. In data transmission, these ghosts produce errors garbled noise or interference for example the cracking noise in mobile phones

## Slide 7: Bandwidth and Spectrum
  C = Maximum possible transmission speed in the channel (bps)
  B = Bandwidth (Hz)
  S/N = Signal-to-Noise Ratio
Shannon equation
  C=B Log2 (1+S/N)
Higher B higher C
Commercial mobile services operate in the “Golden Zone”
High MHz to Low GHz range
Amount of frequency spectrum is limited
Use Spread spectrum transmission
Notes: Golden zone is the High MHz range to t
This is a catch 22 situation
At higher frequencies, there is more available bandwidth
At lower frequencies, signals propagate better
Frequencies are high enough for there to be large total bandwidth so there is bandwidth available
Frequencies are low enough to allow fairly good propagation characteristics, higher frequencies are prone to interference and attenuation
There is a need to take the most advantage of this situation, spectrum in the Golden Zone is limited and very expensive therefore there is a problem regarding the use of bandwidth to increase data rate for this reason the maximum data rate in WLAN is not more than 100Mbps

## Slide 8: WLAN Components
Wireless NIC (WNIC)
Access Points (AP)
Antennae
Notes: WNIC a card that functions as a transceiver
AP is an Ethernet port plus a tranceiver, connected to the wired network infraestructure and a set of wireless end stations, acts a a bridge between wired and wireless LAN and perform basic routing functions
Antennae are usually Omni directional but can be also directional ones

## Slide 9: IEEE 802.11 architecture
Basic Service Set (BSS)
  Independent BSS (IBSS) does not use access point
  IBSS known as Ad-Hoc Network (peer-to-peer communication)
  When BSS are connected to the network becomes one with infraestucture
  Interconnected using a Distribution System through the access points (AP)
Notes: A BSS that stands alone and is not connected to a base is called an Independent Basic Service Set (IBSS) or is referred to as an Ad-Hoc Network. An ad-hoc network is a network where stations communicate only peer to peer. There is no base and no one gives permission to talk. Mostly these networks are spontaneous and can be set up rapidly. Ad-Hoc or IBSS networks are characteristically limited both temporally and spatially
When BSS's are interconnected the network becomes one with infrastructure. 802.11 infrastructure has several elements. Two or more BSS's are interconnected using a Distribution System or DS. This concept of DS increases network coverage. Each BSS becomes a component of an extended, larger network. Entry to the DS is accomplished with the use of Access Points (AP). An access point is a station, thus addressable. So, data moves between the BSS and the DS with the help of these access points

## Slide 10: IEEE 802.11 architecture
Extended Service Set (ESS)
  Next level of hierarchy of BSS
  One or more access points provide a larger service area
  Looks like an independent BSS set to the LLC layer
Notes: Creating large and complex networks using BSS's and DS's leads us to the next level of hierarchy, the Extended Service Set or ESS. The beauty of the ESS is the entire network looks like an independent basic service set to the Logical Link Control layer (LLC). This means that stations within the ESS can communicate or even move between BSS′s transparently to the LLC.

## Slide 11: IEEE 802.11 architecture
Multiple-Cell Wireless LAN
  ESS with two or more APs
  A mobile station moves from one AP coverage area to another without loss of connectivity
  Also called “roaming”
  Analogous to cellular phone transmission
Notes: A cell broadcast area is around a single AP, each cell uses a different set of frequencies between the mobile station and the AP
A mobile station moves from one AP coverage area to another without interruption in service or loss in connectivity loss of connectivity is called “roaming

## Slide 12: Transmission and Media Access Control
IEEE 802.11 operates within the 2.4GHz ISM band
All stations and their APs share a single channel
Only one station or AP can transmit at a time
Access control uses:
  CSMA/CD+ACK (mandatory)
  RTS/CTS (optional )
Notes: The radio-based standards operate within the 2.4 GHz ISM band. These frequency bands are recognized by international regulatory agencies radio operations. As such, 802.11-based products do not require user licensing or special training.
Spread-spectrum techniques, in addition to satisfying regulatory requirements, increase reliability, boost throughput, and allow many unrelated products to share the spectrum without explicit cooperation and with minimal interference.
The original 802.11 wireless standard defines data rates of 1 Mbps and 2 Mbps via radio waves using frequency hopping spread spectrum (FHSS) or direct sequence spread spectrum (DSSS). It is important to note that FHSS and DSSS are fundamentally different signaling mechanisms and will not interoperate with one another.
Using the frequency hopping technique, the 2.4 GHz band is divided into 75 1-MHz subchannels. The sender and receiver agree on a hopping pattern, and data is sent over a sequence of the subchannels. Each conversation within the 802.11 network occurs over a different hopping pattern, and the patterns are designed to minimize the chance of two senders using the same subchannel simultaneously.
FHSS techniques allow for a relatively simple radio design, but are limited to speeds of no higher than 2 Mbps. This limitation is driven primarily by FCC (Federal Communications Commission USA) regulations that restrict subchannel bandwidth to 1 MHz. These regulations force FHSS systems to spread their usage across the entire 2.4 GHz band, meaning they must hop often, which leads to a high amount of hopping overhead.
In contrast, the direct sequence signaling technique divides the 2.4 GHz band into 14 22-MHz channels. Adjacent channels overlap one another partially, with three of the 14 being completely non-overlapping. Data is sent across one of these 22 MHz channels without hopping to other channels.
To compensate for noise on a given channel, a technique called “chipping” is used. Each bit of user data is converted into a series of redundant bit patterns called “chips.” The inherent redundancy of each chip combined with spreading the signal across the 22 MHz channel provides for a form of error checking and correction; even if part of the signal is damaged, it can still be recovered in many cases, minimizing the need for retransmissions

## Slide 13: CDMA/CA+ACK operation
Wireless uses Carrier Sense Multiple Access Collision Avoidance with Acknowledgment (CDMA/CA+ACK) rather than CDMA/CD (Collision Detection.)
Notes: CSMA/CA+ACK works as follows. A station wishing to transmit senses the air, and, if no activity is detected, the station waits an additional, randomly selected period of time and then transmits if the medium is still free. If the packet is received intact, the receiving station issues an ACK frame that, once successfully received by the sender, completes the process. If the ACK frame is not detected by the sending station, either because the original data packet was not received intact or the ACK was not received intact, a collision is assumed to have occurred and the data packet is transmitted again after waiting another random amount of time
CSMA/CA thus provides a way of sharing access over the air. This explicit ACK mechanism also handles interference and other radio related problems very effectively. However, it does add some overhead to 802.11 that 802.3 does not have, so that an 802.11 LAN will always have slower performance than an equivalent Ethernet LAN.

## Slide 14: RTS/CTS Operation
Server
Switch
Laptop
Access
Point B
Large Wired LAN
Radio
Link
Client PC
2. Access point broadcasts
a Clear-to-Send message.
Station that sent the RTS
may transmit unimpeded.
Other stations hearing the CTS must wait
CTS
RTS
1. Device that wishes
to transmit may send a
Request-to-Send message
Notes: Another MAC-layer problem specific to wireless is the “hidden node” issue, in which two stations on opposite sides of an access point can both “hear” activity from an access point, but not from each other, usually due to distance or an obstruction.
To solve this problem, 802.11 specifies an optional Request to Send/Clear to Send (RTS/CTS) protocol at the MAC layer. When this feature is in use, a sending station transmits an RTS and waits for the access point to reply with a CTS. Since all stations in the network can hear the access point, the CTS causes them to delay any intended transmissions, allowing the sending station to transmit and receive a packet acknowledgment without any chance of collision.
Since RTS/CTS adds additional overhead to the network by temporarily reserving the medium, it is typically used only on the largest-sized packets, for which retransmission would be expensive from a bandwidth standpoint.

## Slide 15: IEEE 802.11 group
Notes: The 802.11 family currently includes six over-the-air modulation techniques that all use the same protocol. The most popular (and prolific) techniques are those defined by the b, a, and g amendments to the original standard; security was originally included and was later enhanced via the 802.11i amendment. Other standards in the family (c–f, h–j, n) are service enhancements and extensions or corrections to previous specifications. 802.11b was the first widely accepted wireless networking standard, followed (somewhat counterintuitively) by 802.11a and 802.11g.
The term 802.11x is also used to denote this set of standards and is not to be mistaken for any one of its elements. There is no single 802.11x standard. The term IEEE 802.11 is also used to refer to the original 802.11, which is now sometimes called "802.11legacy."

## Slide 16: IEEE 802.11b
The most widely used standard and the first to become popular
Products that adhere to this standard are considered “WiFi Certified”
Has an speed of 11Mbps
Signal range is best and not easily obstructed due to its low frequency
Not interoperable with 802.11a due to different frequencies
Only 3 non-overlapping channels, supports fewer simultaneous users
Useful for the home market because of its inability to avoid APs conflicts and its low cost
Notes: The most widely used standard and the first to become popular, IEEE802.11b has a rate speed up to 11Mbps although actual throughput shared by all devices is only half the speed,
Operates in the 2.4GHz band where all NICs and APs operate at this frequency, therefore throughput does not fall sharply with distance as it does with 802.11a therefore it requiere fewer access points for coverage of large areas
Its signal range is best and not easly obstructed due to its low frequency
It is not interoperable with 802.11a because 802.11a and 802.11b uses different frequencies
There are 14 channels available in the 2.4GHz band however there are only 3 non-overlapping channels, therefore it support fewer simultaneous users and interfere with each other reducing each user’s throughput
In a larger 3D building its imposible to avoid acces points conflicts hence 802.11b is better served for the home market
Low cost

## Slide 17: IEEE 802.11a
Maximum speed up to 54Mbps, operates in the 5Ghz band
All products that adhere to this standard are considered “WiFi Certified”
Eight available non-overlapping channels, may offer 14 in the future, support more simultaneous users
Shorter range than 802.11b due to its higher frequency
Not interoperable with 802.11b
Higher cost and mostly used in the business market
Notes: Has fastest maximums speed up to 54Mbps, operates in the 5Ghz band
All products that adhere to this standard are considered “WiFi Certified”
Has eight available non-overlapping channels and may offer 14 in the future, therefore it support more simultaneous users
Shorter range than 802.11b due to its higher frequency
Not interoperable with 802.11b
Higher cost and mostly used in the business market

## Slide 18: IEEE 802.11g
Operates in the 2.4GHz band, throughput of 802.11g falls off more slowly than 802.11a throughput
Maximum speed up to 54Mpbs
Compatible with 802.11b, both standard use the same frequency
More improved security enhancements over 802.11 and supports more simultaneous uses
Signal range is best and is not easily obstructed
14 channels available in the 2.4GHz band, only three non-overlapping channels, appliances may interfere on the unregulated signal frequency
More expensive than 802.11b
Notes: Operates in the lower 2.4GHz band therefore throughput of 802.11g falls of more slowly than 802.11a throughput
Reaches a maximum speed up to 54Mpbs and its compatible with 802.11b because both standard use the same frequency
It has more improved security enhancements over 802.11 and supports more simultaneous uses
The signal range is best and is not easily obstructed
14 channels available in the 2.4GHz band with only three non-overlaping channels, appliances may interfere on the unregulated signal frequency
More expensive than 802.11b

## Slide 19: Characteristics of 802.11a/b/g

## Slide 20: 802.11 Security
In older products the installation default was to have no security at all
Wired Equivalent Privacy (WEP)
  Security protocol for WLAN defined in the 802.11b standard
  Encrypts data over radio so it is protected ad it is transmitted from one end point to another
  The two stations uses the same encryption key, shared key
  With so much traffic generated with one unchanging key, hackers can crack the key by collecting data for a few days
  Once the key is cracked, the attacker can read all messages and send attack messages into the network without going through a firewall filter
  Software that automates the hacking process is widely available on the net
  Can be improved by adding VPN but it is more expensive
Notes:   Shared static keys means that a large volume of traffic is encrypted with the same key
  With so much traffic generated with one unchanging key, hackers can crack the key by collecting data for a few days
  Once the key is cracked, the attacker can read all messages and send attack messages into the network without going through a firewall filter

## Slide 21: 802.11 Security
Wi-Fi Protected Access (WPA)
  Wi-Fi standard introduced in 2002 to improve the security flaws of WEP
  Designed to work with existing Wi-Fi products that have WEP, i.e as a software upgrade to existing hardware
  Uses Temporary Key Integrity Protocol (TKIP) and Extensible Authentication Protocol (EAP), features from IEEE802.11i standard
Notes:   Temporary Key Integrity Protocol (TKIP) and Exensible Authentication Portocol (EAP), features from IEEE802.11i standard is introduced for products build in 2002 and 2003, it actually acts as an upgrade of WEP because WPA is fully compatible with WEP

## Slide 22: 802.11 Security
IEEE 802.11i security
  Full security mechanism introduced in 2003
  802.11i specifies Temporal Key Integrity Protocol (TKIP)
    TKIP scrambles the keys using a hashing algorithm and by adding an integrity-checking feature, ensures that the keys have not been tampered with.
  802.11i specifies Expensively Authentication Protocol (EAP)
    Authentication is one party, providing its identification ato the other party
    Authenticate with an authentication server, checks authentication data and sends back an affirmation or rejectio message

## Slide 23: IEEE 802.15
Designed to enable short range wireless connectivity for mobile devices, consumer electronics and computers
Wireless USB – wireless equivalent to current wired USB
Bluetooth – low power, low cost
ZigBee – low power, low cost

## Slide 24: Wireless USB – IEEE802.15.3a
Very new standard - yet to be finalised
Intends to provide a method whereby current peripheral devices will be able to intelligently connect without wires
Star topology with up to 127 devices per controlling device
Speeds of 480Mbps @ 3m & 110Mbps @ 10m

## Slide 25: IEEE 802.15.1 – Bluetooth
Primary use in providing connectivity for battery powered devices such as laptops, cameras, PDAs, mobile phones, mobile phone headsets etc.
Star network topology with 8 devices including master node per PAN

## Slide 26: Bluetooth
Uses FHSS at the 2.45GHz ISM band using 79 channels between 2.402-2.480 GHz
Range is from 10cm up to 10 metres and power consumption of 0dBm
Can be increased up to 100 meters by amplifying power to 20dBm
Excellent for mobility
Does not support TCP/IP and wireless LAN applications well
Very slow, maximum speed 722kbps
Notes: Bluetooth is the name given to a new technology standard using short-range radio links, intended to replace the cable(s) connecting portable and/or fixed electronic devices. The standard defines a uniform structure for a wide range of devices to communicate with each other, with minimal user effort.
Bluetooth uses Frequency Hop Spread Spectrum (FHSS) to avoid any interference. A Bluetooth channel is divided into time slots each 625 micro second in length. The devices hop through these timeslots making 1600 hops per second. This trades bandwidth efficiency for reliability, integrity and security
Bluetooth radios operate in the unlicensed ISM band at 2.4 Gigahertz using 79 channels between 2.402 GHz to 2.480 GHz. The range for Bluetooth communication is 10cm to10 meters with a power consumption of 0dBm (1mW). This distance can be increased to 100 meters by amplifying the power to 20dBm. The Bluetooth radio system is optimized for mobility

## Slide 27: Bluetooth Architecture
Each radio has 48-bit unique device address (BD_ADDR) that is fixed
Each active device within a piconet is identifiable by a 3-bit active device address
Inactive slaves in unconnected modes may continue to reside within the piconet
A master is the only one that may initiate a Bluetooth communication link
Slaves are not allowed to talk to each other directly
Once a link is established, the slave may request a master/slave switch to become the master
Each piconet uses a different frequency hopping sequence.
Radio devices used TDM.
A master device in a piconet transmits on even numbered slots and the slaves may transmit on odd numbered slots
Notes: Bluetooth communication occurs between a master radio and a slave radio. Bluetooth radios are symmetric in that the same device may operate as a master and also the slave. Each radio has a 48-bit unique device address (BD_ADDR) that is fixed.
Two or more radio devices together form ad-hoc networks called piconets. All units within a piconet share the same channel. Each piconet has one master device and one or more slaves. There may be up to seven active slaves at a time within a piconet. Thus, each active device within a piconet is identifiable by a 3-bit active device address. Inactive slaves in unconnected modes may continue to reside within the piconet.
A master is the only one that may initiate a Bluetooth communication link. However, once a link is established, the slave may request a master/slave switch to become the master. Slaves are not allowed to talk to each other directly. All communication occurs within the slave and the master. Slaves within a piconet must also synchronize their internal clocks and frequency hops with that of the master. Each piconet uses a different frequency hopping sequence. Radio devices used Time Division Multiplexing (TDM). A master device in a piconet transmits on even numbered slots and the slaves may transmit on odd numbered slots

## Slide 28: IEEE 802.15.4 – ZigBee
Ultra Low powered digital radios
Used in monitoring and control
16bit or 64bit addressing
A variety of topologies available
  Star
  Point to point
  Dynamic (self-healing) Mesh
DSSS & 128bit encryption
Notes: Though WPAN implies a reach of only a few meters, 30 feet in the case of ZigBee, the network will have several layers, so designed as to enable intrapersonal communication within the network, connection to a network of higher level and ultimately an uplink to the Web. The ZigBee Standard has evolved standardized sets of solutions, called ‘layers'. These layers facilitate the features that make ZigBee very attractive: low cost, easy implementation, reliable data transfer, short-range operations, very low power consumption and adequate security features. 1. Network and Application Support layer : The network layer permits growth of network sans high power transmitters. This layer can handle huge numbers of nodes. This level in the ZigBee architecture includes the ZigBee Device Object (ZDO), user-defined application profile(s) and the Application Support (APS) sub-layer.
The APS sub-layer's responsibilities include maintenance of tables that enable matching between two devices and communication among them, and also discovery, the aspect that identifies other devices that operate in the operating space of any device.
The responsibility of determining the nature of the device (Coordinator / FFD or RFD) in the network, commencing and replying to binding requests and ensuring a secure relationship between devices rests with the ZDO (Zigbee Define Object). The user-defined application refers to the end device that conforms to the ZigBee Standard.
2. Physical (PHY) layer : The IEEE802.15.4 PHY physical layer accommodates high levels of integration by using direct sequence to permit simplicity in the analog circuitry and enable cheaper implementations.
3. Media access control (MAC) layer : The IEEE802.15.4 MAC media access control layer permits use of several topologies without introducing complexity and is meant to work with large numbers of devices.

## Slide 29: ZigBee Architecture
Devices perform a number of roles in the network
Adding devices to network extends range
Coordinator node tests network for shortest path and least congested route for data

## Slide 30: Summary of Standards
Standard | ZigBee™ | Wi-Fi™ | Bluetooth™
 | 802.15.4 | 802.11b | 802.15.1
Transmission Range (meters) | 1 – 100 | 1 - 100 | 1 – 100
Battery Life (days) | 100 – 1,000 | 0.5 – 5.0 | 1-7
Network Size (# of nodes) | > 64,000 (with 64bit addressing) | 32 | 7
Application | Monitoring & Control | Web, Email, Video | Cable Replacement
Stack Size (KB) | 4 – 32 | 1,000 | 250
Throughput kb/s) | 20 – 250 | 11,000 | 720
Table from http://www.maxstream.net/wireless/zigbee.php

## Slide 31: Questions