## Slide 1: The Ethernet
Team 2:
Adelmo Amarö
David Congreve
Chris McKeague
Joel Schrader

## Slide 2: Background
The term Ethernet refers to the family of local-area network (LAN) products covered by the IEEE 802.3 standard
Three data rates are currently defined for operation over optical fibre and twisted-pair cables:
• 10 Mbps—10Base-T Ethernet
• 100 Mbps—Fast Ethernet
• 1000 Mbps—Gigabit Ethernet

## Slide 3: Benefits
Is easy to understand, implement, manage, and maintain
Allows low-cost network implementations
Provides extensive topological flexibility for network installation
Guarantees successful interconnection and operation of standards-compliant products, regardless of manufacturer

## Slide 4: Topologies and Structures
3 basic interconnection structures or network building blocks:
• Point-to-Point Interconnection
• Coaxial Bus Topology
• Star-Connected Topology

## Slide 5: IEEE802.3 Logical Relationship to the ISO Reference Model

## Slide 6: Basic Data Communication between MAC and Physical Layer

## Slide 7: The Ethernet MAC Sublayer
Purpose
Data encapsulation and media access control
Topics presented
Ethernet frame format
Frame transmission
Frame reception

## Slide 8: Ethernet Frame Format
Defined by IEEE 802.3

## Slide 9: Ethernet Frame Transmission
Half Duplex Transmission - CSMA/CD Access Method
Carrier Sense – listen for traffic on medium
Multiple Access – transmitting enabled on trafficless network
Collision Detect – transmitting stations capable of detecting collisions

## Slide 10: Ethernet Frame Transmission
Full Duplex Transmission
Simple
No collisions
No scheduled retransmission
Only restricted by interframe gap between successive frames

## Slide 11: Ethernet Frame Reception
Similar for both half and full duplex
Reverse of Frame transmission
Sent and received Frame checking

## Slide 12: Ethernet Physical layers
Ethernet devices uses NIC connected to the motherboard
Indicates by the following convention

## Slide 13: The 802.3 Physical Layer Relationship to ISO Model
Physical layer divided into independent sub layers
  Reconciliation sub layer and MII (Media Independent Interface)
  Media-dependent physical coding sub layer (PCS)
  Physical medium attachment (PMA) sub layer
  Medium-dependent interface (MDI)
  Auto-negotiation sub layer

## Slide 14: The 802.3 Physical Layer Relationship to ISO Model

## Slide 15: 10 Mbps Ethernet Standards
IEEE 802.3 standard
Systems
  10BaseT (Twisted-Pair Ethernet)
  10Base2 (Thinnet)
  10Base5 (Thicknet)

## Slide 16: 100 Mbps Ethernet Standards
10Base-T
  Run over 4 wires
  Star wired topology
  Uses Cat-3 or Cat -5 UTP
  Can support full or half duplex communication
  100m maximum length
  A hub or switch sits in the middle, has a port for each node.

## Slide 17: 100 Mbps Ethernet Standards
10Base-T

## Slide 18: 10 Mbps Ethernet Standards
10Base5
  Original 10Mbps implementation of Ethernet
  Uses 75 Ω RG 8 coaxial cable, maximum length 500m
  Bus topology
  Need 50 Ω terminators at each end.
  Almost extinct

## Slide 19: 10 Mbps Ethernet Standards
10Base5

## Slide 20: 10 Mbps Ethernet Standards
10Base2
  Uses 50 Ω RG-58 coaxial cable, maximum length 200m
  Bus topology
  Uses BNC-T connectors at the end of each device
  Need 50 Ω terminators at each end.
  Almost extinct

## Slide 21: 10 Mbps Ethernet Standards
10Base2

## Slide 22: 100 Mbps Fast Ethernet Standards
IEEE 802.3 standard
Systems:
  100Base X Media
  100Base T4

## Slide 23: 100Base –X Media
Two physical medium specifications
100Base-TX
  Uses Cat-5 UTP cable
  Star shape topology
  Can achieve up to 200Mbps at full duplex
100Base-FX
  Uses two sets of multimode fibre optic cable, one for Tx and one for Rx
  400m half-duplex, 2km full duplex

## Slide 24: 100Base –T4
Uses Cat-3 UTP
Developed to allow 10BaseT to be upgraded to 100-Mbps without replacing Cat-3 UTP with Cat-5 UTP
Uses all 4 pairs in the cable
Limited to half-duplex
Currently obsolete

## Slide 25: Gigabit Ethernet
IEEE 802.3ab standard
  1000BaseT:
    Uses Cat-5e (enhanced) or Cat-6 UTP
    Maximum length 100m

## Slide 26: Gigabit Ethernet
IEEE 802.3z standard
  1000BaseSX
    Uses multimode fibre
    Maximum length 220m
  1000BaseLX
    Uses long wavelength laser
    Multimode or single mode fibre
    On a single-mode fibre it can reach up to 10 km
  1000BaseCX
    Connects short distances, 25m, UTP
    Obsolete

## Slide 27: Gigabit Ethernet

## Slide 28: Summary of Ethernet Systems

## Slide 29: 10 Gigabit Ethernet
Very new system
Originally specified by a supplementary standard, IEEE 802.3ae
Now, IEEE 802.3-2005 standard
Does not use CSMA/CD
Uses fibre optic

## Slide 30: 10 Gigabit Ethernet

## Slide 31: Summary of Ethernet Standards

## Slide 32: System Considerations
Component Selection
Network Upgrades
Multiple Speed networks
Link Aggregation

## Slide 33: Component Selection & Network Upgrades
Ensure that all connected components are compatible
Auto-negotiation almost eliminates the need to configure connected hardware
Auto-negotiation can be used to provide backwards compatibility, hence allowing gradual upgrades of network infrastructure

## Slide 34: Multiple Speed Networks
Provide greater efficiency and flexibility in the architecture design
Provide high speed backbone to ensure all clients receive best possible connection to servers

## Slide 35: Link Aggregation
Another way of achieving flexibility and efficiency in a network architecture is to use link aggregation to provide 1 virtual connection over multiple physical connections
Commonly used with internet connections to provide a better connection
Can also be used to provide some redundancy (i.e. 2 connections provided by different wholesalers)

## Slide 36: Questions?

## Slide 37: References
Behrouz Forouzan, 2004, Data Communications and Networking, 3rd Edition, McGraw-Hill, NY, USA
Parker Malcolm, Computer Networks, Version 2, North Sydney College of TAFE, 2000, NSW, Australia.
Gilbert Held, 1996, Understanding Data Communications, 5th Edition, Sams Publishing, IN, USA
Ethernet Technologies CISCO http://www.cisco.com/univercd/cc/td/doc/cisintwk/ito_doc/ethernet.pdf
Ethernet, Wikipedia, the free encyclopaedia
http://en.wikipedia.org/wiki/Ethernet
Dr. Song Xing, Fall 2004, CIS 485 Local Area Networks notes, Department of Information Systems, California State University, LA, CA, USA
Dr Rolfe Sassenfeld, Spring 2006, MIT 5330 Computer Networks and Data Communication, class notes, Computer Science Department, The University of Texas at El Paso, TX, USA
http://sassenfeld.cs.utep.edu/mit5330/index.htm
Connected: an Internet Encyclopaedia, Ethernet
http://www.freesoft.org/CIE/Topics/60.htm